## Slide 1
Preempt-RT Raspberry Linux
VMware Tiejun Chen <tiejunc@vmware.com>

## Slide 2: The declaration of this development
This is my personal exploration.
This is not a roadmap or commitment from VMware.

## Slide 3: Agenda
Motivation
Raspberry Pi platform
Real Time characteristics & Preempt-RT Linux
Preempt-RT Raspberry Linux
Evaluation
Roadmap

## Slide 4: Motivation
IoT is supposed to be the next big thing.
Raspberry pi is one popular open source hardware.
Linux is more often found on IoT devices and gateways.
Linux-based Raspberry pi is fantastic in the case of IoT.
But IoT needs to consider Real-Time characteristic.
A part of my plan of EPLE - Enabling Preempt-RT Linux Everywhere
  Preempt-rt rpi Linux
  Preempt-rt Linuxkit
  …

## Slide 5: Raspberry Pi overview
The Raspberry Pi is a series of small single-board computers developed in the United Kingdom by the Raspberry Pi Foundation to promote the teaching of basic computer science in schools and in developing countries. The original model became far more popular than anticipated, selling outside its target market for uses such as robotics. It does not include peripherals (such as keyboards, mice and cases). However, some accessories have been included in several official and unofficial bundles. -- wiki

## Slide 6: Raspberry Pi hardware
BCM2837: Raspberry Pi 3 and Pi 2 (later)
  A quad-core ARM Cortex A53 (ARMv8)
  BCM2836: Raspberry Pi 2
  A quad-core ARM Cortex-A7
  BCM2835: Raspberry Pi 1 and Zero
    ARM 1176
  A small and affordable embedded platform that you can do a lot of things, and put into practice in IoT development.

## Slide 7: Real Time characteristics
What RTOS needs to be Deterministic
  Interrupt & Context switch
  Preemption
  Latency
  Jitter
  Faster ?
Linux mainline kernel was not designed as RTOS

## Slide 8: Preempt-RT Linux patches
This series of patches are aimed at converting Linux as the preemptible kernel
  ~ 100%
  threaded irq
  get preempted in critical section
  quick reaction times!
  bring latencies down to a minimum as very possible
  It’s likely a hard real-time extensions mostly.

## Slide 9: Preempt-RT Linux vs Mainline Linux
Many features are already merged into mainline.
  High resolution timers
  Interrupt threads
  Mutex
  …
  Outsider
    The conversion of spinning locks into sleeping locks

## Slide 10: Raspberry Pi Linux
raspberrypi/Linux
  Kernel source tree for Raspberry Pi Foundation-provided kernel builds. Issues unrelated to the Linux kernel should be posted on the community forum at https://www.raspberrypi.org/forum
  https://github.com/raspberrypi/linux

## Slide 11: Raspberry Pi distributions
Raspbian
Ubuntu Mate, Snappy ubuntu core, Windows 10 IoT Core, …
Current Linux / BSD kernels for the Raspberry Pi do not provide preempt-rt feature.

## Slide 12: Preempt-RT Linux Source
The current development -RT tree
  http://git.kernel.org/pub/scm/linux/kernel/git/rt/linux-rt-devel.git
The current stable -RT tree
  https://git.kernel.org/pub/scm/linux/kernel/git/rt/linux-stable-rt.git/
Released stable -RT patchset
  https://www.kernel.org/pub/linux/kernel/projects/rt/4.14/

## Slide 13: Raspberry Pi Preempt-RT Linux tree 1/2
Stage 0: Ready
Fork https://github.com/raspberrypi/linux in github
$ git clone https://github.com/TiejunChina/linux
$ git remote add upstream git@github.com:raspberrypi/linux.git
$ git fetch

## Slide 14: Raspberry Pi Preempt-RT Linux tree 2/2
Stage 1: During development cycle
$ git checkout -b rpi-4.14.y-rt rpi-4.14.y
$ git am all preempt-rt patches on rpi-4.14.y-rt <v4.14.20-rt17>
$ rebase it if any new –rt version is available
Stage 2: During maintaining cycle
$ git am diff between the previous -rt and the new –rt
$ git merge rpi-4.14.y regularly
$ git am any fix specific to rt issue
https://github.com/raspberrypi/Linux/rpi-4.14.y-rt:v4.14.24-rt19

## Slide 15: A few issues 1/2
Rebase some conflicts
  Like “Revert "softirq: Let ksoftirqd do its job“”
Lockup
  “usb: dwc_otg: fix system lockup when interrupts are threaded”
    Oussama Ghorbel ghorbel@gmail.com

## Slide 16: A few issues 2/2
Shared IRQ
  [ 347.337186] Disabling IRQ #59
  IRQ #59 is shared across the AUX peripherals spi1, spi2 and uart1.

## Slide 17: Example: how to build
cross-compiler
  gcc-linaro-7.2.1-2017.11-x86_64_aarch64-linux-gnu
  https://releases.linaro.org/components/toolchain/binaries/latest/aarch64-linux-gnu/
aarch64
  bcmrpi3_defconfig {bcm2709_defconfig/bcmrpi_defconfig}
  Phil Elwell committed this
  make rpm

## Slide 18: Evaluation: cyclctest
Raspberry Pi3 Model B
Based on openSUSE 64bit
  http://download.opensuse.org/ports/aarch64/factory/images/
rt-test
  https://wiki.linuxfoundation.org/realtime/documentation/howto/tools/rt-tests
  Cyclictest
  https://www.osadl.org/uploads/media/mklatencyplot.bash

## Slide 19: RPi Preempt-RT Linux: CONFIG_PREEMPT_NONE
No Forced Preemption
  There are no guarantees and occasional long delays are possible.
Latency (us): max 3629 us

## Slide 20: RPi Preempt-RT Linux: CONFIG_PREEMPT__LL
Preemptible Kernel (Low-Latency Desktop)
  This option reduces the latency of the kernel by making all kernel code (that is not executing in a critical section preemptible. This allows reaction to interactive events by permitting a low priority process to be preempted involuntarily even if it is in kernel mode executing a system call and would otherwise not be about to reach a natural preemption point.
  Latency (us): max 2582 us

## Slide 21: RPi Preempt-RT Linux: CONFIG_PREEMPT_RT_FULL
Fully Preemptible Kernel (RT)
  Everything
  Latency (us): max 141 us

## Slide 22: Test result of RPi Preempt-RT Linux
Low latency significantly
  From 3629 us down to 141 us

## Slide 23: Tips 1/2
Phenomenon
  Higher CPU utilization from irq
    PID USER PR NI VIRT RES SHR S %CPU %MEM TIME+ COMMAND
    70 root -51 0 0 0 0 S 25.00 0.000 0:32.80 irq/41-3f980000
    71 root -51 0 0 0 0 S 20.00 0.000 0:33.41 irq/41-dwc2_hso
  If we have too much interrupts?

## Slide 24: Tips 2/2
What we can do now?
  isolate cpu
    isolcpus=3
  dedicate irq to cpu3
  linux:~ # cat /proc/interrupts
  CPU0 CPU1 CPU2 CPU3
  2: 60182 57004 60988 324 bcm2836-timer 1 Edge arch_timer
  6: 1 0 0 14 ARMCTRL-level 1 Edge 3f00b880.mailbox
  41: 0 0 0 2017824 ARMCTRL-level 41 Edge 3f980000.usb, dwc2_hsotg:usb1
  71: 0 0 0 237523 ARMCTRL-level 88 Edge mmc0

## Slide 25: RPi Preempt-RT Linux: CONFIG_PREEMPT_RT_FULL
Fully Preemptible Kernel (RT)
  Everything
  Latency (us): max 114 us

## Slide 26: Roadmap
More platforms
more tests
  Ltp, lmbench, posix
irq affinity dynamically
virtualization based on preempt-rt Linux
Unilinux -- unikernelized preempt-rt Linux